Making a Magnet

Electricity and Magnetism are Cousins

# What is Needed

- A dry cell cell battery

- A few feet of thin insulated wire (~28-32 gauge)

- A magnetic compass

- A steel rod or nail a few inches long

- Some tape

# What to Do

Remove some insulation from each end of the wire.  Wind the wire around the steel rod forming a coil.  Use some tape to hold the wire to the rod.

Lay the rod on the table and bring the magnetic compass near one end of the rod.  Make sure that the needle of the compass is not pointing at the end of the rod.  The needle should be pointing North, so lay the rod so it runs East to West.

Tape one end of the wire to one end of the battery.  Look at the compass while you touch the other end of the wire to the opposite end of the battery.  What happens?  Don’t leave the wire in contact too long or the battery will run down.

# What is Happening?

Purdue University

Department of Physics

Physics on the Road Hands-On