TORNADOS
Why does the air in a tornado spin?

# _____________________________________________________________

# What is Needed

- Two 2-liter pop bottles connected

________________________________________________________________________

# What to Do

To start the tornado action, grab the end of the full bottle and rotate in a circular motion until a vortex (spinning) begins.  This can be repeated again and again.  The direction of rotation can be either clockwise or counterclockwise.

________________________________________________________________________

What is Happening?

Tornados, whirlpools, waterspouts, and similar motions in fluids that occur when liquid drops through an opening are called vortexes.  The action is the concentration of kinetic energy (motion of the fluid).  In the atmosphere, thermals and wind shear are the source of the energy which produces the tornado vortex.

In liquids, such as water, the potential energy (mass) is converted into kinetic energy (motion) as it descends, pulled by gravity through an opening.  A small initial rotation about the opening becomes more violent (higher rotational velocity) as the molecules come closer to the center.  The resulting outward force tends to keep the liquid out of the exact center, maintaining a “hole” in the remaining liquid.

Purdue University

Department of Physics

Physics on the Road Hands-On